## Slide 1: Accelerated Architectures
EPCC
The University of Edinburgh

## Slide 2: Outline
Why do we want/need accelerators such as GPUs?
Architectural reasons for accelerator performance advantages
Latest accelerator Products
  (current) Market leader: NVIDIA
  Alternatives: AMD GPUs, Intel Xeon Phi
Accelerated Systems
Notes: Why need, why good, How do we make supercomputers

## Slide 3: 4 key performance factors
Memory
Processor
DATA IN
DATA OUT
DATA PROCESSED
Amount of data processed at one time (Parallel processing)
Processing speed on each data element (Clock frequency)
Amount of data transferred at one time (Memory bandwidth)
Time for each data element to be transferred (Memory latency)
Notes: Here we have pic of proc –don’t know more yet –
Has to be attached to mem
Mem in, process, mem out
Interested in how fast it can be done

## Slide 4: 4 key performance factors
Memory
Processor
DATA IN
DATA OUT
DATA PROCESSED
Parallel processing
Clock frequency
Memory bandwidth
Memory latency
Different computational problems are sensitive to these in different ways from one another
Different architectures address these factors in different ways

## Slide 5: CPUs: 4 key factors
Parallel processing
  Until relatively recently, each CPU only had a single core. Now CPUs have multiple cores, where each can process multiple instructions per cycle
Clock frequency
  CPUs aim to maximise clock frequency, but this has now hit a limit due to power restrictions (more later)
Memory bandwidth
  CPUs use regular DDR memory, which has limited bandwidth
Memory latency
  Latency from DDR is high, but CPUs strive to hide the latency through:
    Large on-chip low-latency caches to stage data
    Multithreading
    Out-of-order execution
Notes: Take CPUs for start
Multi-level parallel –vector per core, multi-core
Freq used to increase

## Slide 6: The Problem with CPUs
The power used by a CPU core is proportional to Clock Frequency x Voltage2
In the past, computers got faster by increasing the frequency
  Voltage was decreased to keep power reasonable.
Now, voltage cannot be decreased any further
  1s and 0s in a system are represented by different voltages
  Reducing overall voltage further would reduce this difference to a point where 0s and 1s cannot be properly distinguished
Notes: Fundamental problem with CPUs power/energy

## Slide 7: The Problem with CPUs
http://queue.acm.org/detail.cfm?id=2181798
Notes: Fundamental problem with CPUs power/energy

## Slide 8: The Problem with CPUs
Instead, performance increases can be achieved through exploiting parallelism
Need a chip which can perform many parallel operations every clock cycle
  Many cores and/or many operations per core
Want to keep power/core as low as possible
Much of the power expended by CPU cores is on functionality not generally that useful for HPC
  e.g. branch prediction

## Slide 9: Accelerators
So, for HPC, we want chips with simple, low power, number-crunching cores
But we need our machine to do other things as well as the number crunching
  Run an operating system, perform I/O, set up calculation etc
Solution: “Hybrid” system containing both CPU and “accelerator” chips

## Slide 10: Accelerators
It costs a huge amount of money to design and fabricate new chips
  Not feasible for relatively small HPC market
Luckily, over the last few years, Graphics Processing Units (GPUs) have evolved for the highly lucrative gaming market
  And largely possess the right characteristics for HPC
    Many number-crunching cores
GPU vendors NVIDIA and AMD have tailored existing GPU architectures to the HPC market
GPUs now firmly established in HPC industry

## Slide 11: Accelerators
Intel released a different type of accelerator to compete with GPUs for scientific computing
  Many Integrated Core (MIC) architecture
  AKA Xeon Phi (codenames Larrabee, Knights Ferry, Knights Corner, Knights Landing)
  Intel prefered the term “coprocessor” to “accelerator”
KNC comprised old Pentium CPU cores from 1993
  Augmented with wide vector units
So again uses concept of many simple low-power cores
  Each performing multiple operations per cycle
Intel Xeon Phi KNH cancelled:
  End of Xeon Phi era

## Slide 12: Latest Technology
NVIDIA
  Volta GPUs have evolved from GeForce series
AMD
  FirePro HPC specific GPUs have evolved from (ATI) Radeon series
Intel
  Xeon Phi emerged to compete with GPUs for general purpose computation
Image: https://www.amd.com/en/products/servers-graphics?utm_medium=redirect&utm_source=301
Image: https://www.nvidia.com/en-us/data-center/tesla-v100/
Image: https://software.intel.com/en-us/xeon-phi/mic

## Slide 13: Accelerators addressing performance
Parallel processing and clock frequency:
  Focus on many number crunching cores.
    (instead of few high-power cores)

## Slide 14: AMD 12-core CPU
Not much space on CPU is dedicated to compute
= compute unit
(= core)

## Slide 15: NVIDIA Pascal GPU
GPU dedicates much more space to compute
  At expense of caches, controllers, sophistication etc
= compute unit
(= SM
= 64 CUDA cores)

## Slide 16: Intel Xeon Phi
As does Xeon Phi
= compute
unit
(= core)

## Slide 17: Accelerators addressing performance
Parallel processing and clock frequency:
  Focus on many number crunching cores.
    (instead of few high-power cores)
Memory bandwidth and latency:
  GDDR and later HBM offer significantly higher bandwidth vs DDR
  Latency hidden by high parallelism, low cost context switching and (some) cache memory.

## Slide 18: Memory
GPUs and Intel Xeon Phi both uses Graphics memory: much higher bandwidth
CPUs use DRAM
GPUs and Xeon Phi
use Graphics DRAM
For many applications, performance is very sensitive to memory bandwidth

## Slide 19: Memory
NVIDIA Pascal introduced stacked memory
Cross-section Photomicrograph of a P100 HBM2 stack and GP100 GPU
Similar staked memory used in Intel KNL (last version of Xeon Phi) and newer GPUs
(Image credits: NVIDIA Pascal architecture White Paper https://images.nvidia.com/content/pdf/tesla/whitepaper/pascal-architecture-whitepaper.pdf )

## Slide 20: Accelerators: 4 key factors
Parallel processing
  Accelerators have a much higher extent of parallelism than CPUs. Many more cores and/or operations per core
Clock frequency
  Accelerators typically have lower clock-frequency than CPUs, and instead get performance through parallelism
Memory bandwidth
  Accelerators use high bandwidth GDDR memory or HBM2 memory
Memory latency
  Memory latency from GDDR is similar to DDR
  GPUs hide latency through very high levels of multithreading
  Xeon Phi hides latency in a similar way to CPUs, although the caches are smaller and no out-of-order execution (in current models).

## Slide 21
GPU performance has been increasing much more rapidly than CPU
Image: https://arxiv.org/pdf/1412.7789.pdf

## Slide 22: GPUs accelerated systems
DRAM
GPUs cannot be used instead of CPUs
    They must be used together
    GPUs act as accelerators
      Responsible for the computationally expensive parts of the code
    CPU-GPU communication (BW/latency) presents bottleneck
CPU
GPU
I/O
I/O
HBM

## Slide 23: GPUs accelerated systems
Performance considerations
  Need to exploit high level of parallelism
  Generally speaking: separate CPU-GPU memory space
    Need to consider transfer to/from GPU-CPU
  HBM generally lower capacity than DDR per GPU/CPU
  Added complexity of programming model
    Need to take the above into consideration
    For GPU Cuda, OpenCL
    OpenMP or OpenACC
    for directives based approach.
    Libraries and high level
    programming languages can help.
DRAM
CPU
HBM
GPU
I/O
I/O

## Slide 24: Xeon Phi accelerated systems
Xeon Phi run their own OS
  Xeon Phi more independent from CPU
  KNC was “card” accelerator and could run in three modes:
    Offload: Highly parallel regions ”offloaded” to XeonPhi similar to GPU acceleration
    Native mode: Log into Xeon Phi card and run directly on KNC
    Symmetric: Run across CPU+KNC as if across nodes
  KNL only available in socket version
    Replaced CPU completely
DRAM
KNL
HBM2
I/O
DRAM
CPU
GDRAM
KNC
I/O
I/O

## Slide 25: NVIDIA Volta look inside
NVIDIA’s latest GPU product is highly AI/DL oriented
Follows basic building blocks of previous architectures with notable improvements
Image courtesy of Alan Grey, NVIDIA

## Slide 26: NVIDIA Volta
Volta GV100 SM
  Chip partitioned into Streaming Multiprocessors (SMs) that act independently of each other
  4 processing blocks per SM, each with:
    16 FP32 Cores
    8 FP64 Cores
    16 INT32 Cores
    2 Tensor cores
    L0 instruction cache
    1 warp scheduler
    1 dispatch unit
    64 KB Register File.
  Number of SMs, and processing blocks etc per SM, varies across products. High-end GPUs have more than 1,000 total “cores”
Image courtesy of Alan Grey, NVIDIA

## Slide 27: NVIDIA Volta
Volta GV100 HBM2
  Up to eight memory dies per HBM2 stack
  Up to four stacks
  Maximum of 32 GB of GPU memory.
Image: https://www.eteknix.com/samsung-sk-hynix-supply-hbm2-nvidia/

## Slide 28: NVIDIA Volta
Volta GV100 HBM2
  Up to eight memory dies per HBM2 stack
  Up to four stacks
  Maximum of 32 GB of GPU memory.
Cache
  128KB configurable
    Data Cache and/or
    Shared memory
    For example, if shared memory is configured to 64 KB, texture and load/store operations can use the remaining 64 KB of L1.
Image courtesy of Alan Grey, NVIDIA

## Slide 29: NVIDIA Volta
NVLink
  Proprietary NVIDIA interconnect
    Introduced with Pascal generation GPUs
    Each NVLink connection achieving approximately 50GB/sec
  Single V100 can support 6 NVlink connections
    Achieving up to 300GB/sec
    3x that of PCIe Gen 3
  Can be used for GPU-GPU communication
  Can also be used for CPU-GPU communication
    (Currently) only with IBM Power CPU
    Notably not available with Intel CPUs

## Slide 30: NVIDIA Volta
NVLink
Image: https://www.nvidia.com/en-us/data-center/nvlink/

## Slide 31: NVIDIA Volta for DL
Tensor cores
  Matrix multiply engines
    Each Tensor Core performs the following operation: D = AxB + C, where A, B, C, and D are 4x4 matrices. The matrix multiply inputs A and B are FP16 matrices, while the accumulation matrices C and D may be FP16 or FP32 matrices.
  Exploit “forgiving” nature of DL problems
    Might prove useful for some HPC codes
  Each Volta has 640 tensor cores, each performing 64 floating-point fused-multiply-add (FMA) operations per clock
    125TFLOPs for training and inference

## Slide 32: NVIDIA Volta
Tensor cores
Animation: https://www.nvidia.com/en-us/data-center/tensorcore/
Notes: Up to 3x throughput vs Pascal

## Slide 33: NVIDIA Volta
Optimised software
Image courtesy of Alan Grey, NVIDIA

## Slide 34: AMD FirePro
AMD acquired ATI in 2006
AMD FirePro series: derivative of Radeon chips with HPC enhancements
Like NVIDIA, High computational performance and high-bandwidth graphics memory
Currently much less widely used for GPGPU than NVIDIA, because of programming support issues

## Slide 35: Intel Xeon Phi
Intel Pentium P54C cores were originally used in CPUs in 1993
  Simplistic and low-power compared to today’s high-end CPUs
KNL moved from Pentium to Silvermont architecture cores (adapted from Atom mobile range)
  Faster single thread performance
  Also integrating network controllers on chip
Philosophy behind Phi is to dedicate large fraction of silicone to many of these cores
And, similar to GPUs, original Phi used MCDRAM Memory
  Higher memory bandwidth than standard DDR memory used by CPUs
  KNL Stacked MCDRAM : 400GB/sec bandwidth
          KNL to DRAM : ~90GB/sec bandwidth

## Slide 36: Intel Xeon Phi
On KNL, each core has been augmented with two wide 512-bit vector unit
For each clock cycle, each core can operate 2 vectors of size 8 (in double precision)
  Twice the width of 256-bit “AVX” instructions supported by current CPUs
Multiple cores, each performing multiple operations per cycle
Peak performance and memory bandwidth similar to GPUs
Vector units drive performance

## Slide 37: Programming
GPUs
  CUDA: Extensions to the C language which allow interfacing to the hardware (NVIDIA proprietary)
  OpenCL: Similar to CUDA but cross-platform (including AMD and NVIDIA)
  Directives based approach: directives help compiler to automatically create code for GPU. OpenACC and now also new OpenMP 4.0
  Libraries like CuFFT, NVBLAS can also help.
Xeon Phi
  Can just use regular CPU code with OpenMP
    Typically needs work to allow compiler to auto-vectorise efficiently
    Intel specific directives allow offloading to phi, such that fast CPU core can be used for serial parts of code
  Also Intel Thread Building Blocks
  Often need intrinsics to fully exploit performance capabilities
Notes: Intel greatest benefit is also drawback

## Slide 38: GPU Accelerated Systems
DRAM
CPUs and Accelerators are used together
  Communicate over PCIe bus or NVLink
CPU
HBM
Accelerator
PCIe
I/O
I/O
Can also be nvlink

## Slide 39: Scaling to larger systems
Can have multiple CPUs and accelerators within each “workstation” or “shared memory node”
  E.g. 2 CPUs +2 Accelerators (below)
  CPUs share memory, but Accelerators do not
DRAM
CPU
I/O
I/O
CPU
PCIe / nvlink
I/O
I/O
Accelerator +
HBM
Interconnect
Interconnect allows multiple nodes to be connected
Accelerator +
HBM
PCIe / nvlink
nvlink

## Slide 40: GPU Accelerated Supercomputer
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
Acc.+CPU
Node
…
…
…
…
…
…

## Slide 41: DIY GPU Workstation
Just need to slot GPU card into PCI-e
Need to make sure there is enough space and power in workstation

## Slide 42: GPU Servers
Multiple servers can be connected via interconnect
Several vendors offer GPU Servers
Example Configuration:
  4 GPUs plus 2 (multi-core) CPUs

## Slide 43: Summit - ORNL
https://www.olcf.ornl.gov/summit/
https://www.olcf.ornl.gov/summit/
Each node:
2x 22core Power9 CPUs
6x NVIDIA V100 GPUs
512 GB DDR4
Mellanox EDR 100G InfiniBand
x4,608 nodes
Notes: ++ COOLING

## Slide 44: Summit - ORNL
https://www.olcf.ornl.gov/summit/
https://www.olcf.ornl.gov/wp-content/uploads/2018/05/Intro_Summit_System_Overview.pdf
Notes: Point to significance of interconnect

## Slide 45: Summit - ORNL
Number 1 machine in the world
  ~187 PFlop/s peak performance
  ~122 PFlop/s max performance
  ~2,300,000 cores
8.8 MW
Power9 system + GPU + Liquid Cooling
EXAOP (not Flop) DL run already a reality:
  https://www.olcf.ornl.gov/2018/06/08/genomics-code-exceeds-exaops-on-summit-supercomputer/
https://www.olcf.ornl.gov/summit/
Notes: Achieved ExaOp performance on AI applications:
Mixed precision
1.8 EXAOPS or 2 billion billion ops
Even 200 PFLOPS = Earth entire population 305 days to do what Summit = 1 second
HDD: 250PB = 74years HD video
Exascale is looking to build a system which can within a 20-30MW envelope
Though summit is not there, it is making significant leaps forward

## Slide 46: Going forward
Some very interesting developments on the horizon
NVIDIA GPUs are current frontrunner
  5 out of 10 of top10 systems use NVIDIA GPUs
Intel focusing on Intel Xeon CPUs (not to be confused with end-of-life Intel Xeon Phi co-processors)
AMD has shown promising technology but still lags in software support
FPGAs and CPUs with FPGAs are becoming more and more relevant due to power efficiency and performance:
  Not “exactly” an accelerator
  Separate lecture on FPGAs coming in a few weeks

## Slide 47: Summary
Accelerators have higher compute and memory bandwidth capabilities than CPUs
  Silicon dedicated to many simplistic cores
  Use of stacked memory
Accelerators are typically not used alone, but work in tandem with CPUs
Most common are NVIDIA GPUs and Intel Xeon Phis.
  Architectures differ
  AMD also have high performance GPUs, but not so widely used due to programming support
GPU accelerated systems scale from simple workstations to large-scale supercomputers
  And dominate the top10 most powerful systems as of June 2018